## Slide 1
Routing and Switching Architecture
Colorless Metro

## Slide 2: What problems are we trying to solve
  Both the iLEC and Metro 2.0 networks are cost optimized for 1G Services
  We need to invest to scale the Metro for 10G and 100G Services – we can’t afford to strategically invest in both
  Cell Site backhaul (VZ, AT&T, T-Mob ~ 18K ports) will require upgrade from 1G to 10G within 2+yrs
  2700 wire centers in iLEC metro support cell cite backhaul
  T-Mobile has ~4800 tower in ~1600 Wire center
  100G metro require to support 10G Tower
  4% of the Current iLEC Wire center are 100G
  70% of VZ, AT&T, T-Mobile towers are same Serving Wire Centers
  Analysis of supporting T-Mobile cell site backhaul upgrade
  iLEC - $500M+
  Colorless $150M < $200M
  Minimize development and reliance on iLEC OSS systems
  Eliminate duplicity of network and hardware (NIDs) , truck rolls and streamline Access

## Slide 3: Colorless Metro - Strategy
Grow Metro 3.0 as strategic colorless Metro and develop support for “all growth” services
  iLEC Metro will continue to support existing services and speeds - consumer available port capacity
  Grow new and higher speed 10G/100G service on Metro 3.0
Interconnect the Metro with BGP-LU / Option-C NNI – allows service interoperability with a common “Route Target”
Deploy 100G Ethernet Collector Node (ECN) in each iLEC wire center
  Use existing (Orange) systems and process to deploy ECN into the Wire center
  Use Inter office Fiber to build 400G and 100G ECNs into the iLEC Wire center
  Use the iLEC lateral fiber to deploy 10G NID over single fiber to the customer/Cell site towers
    A port/UNI on a NID can be iLEC (green) or National (Red/Blue/Orange/Green) – colorless
Two touch service provisioning
  Node A - ILEC MER/MGR - use existing iLEC provision systems
  Node B - Metro Edge (3.0) – use go forward provisioning and automation
  Automates performance testing Y.1731 , Service turn-up Y.1564
Add new Metro 3.0/iLEC Node inventoried in iLEC systems (barebones/black box)
  Develop a sync-Engine to reconcile inventory between National ARM ( ASPI ) and iLEC ARM
  Real time Reconciliation of port inventory and Customer Facing Service (CFS)
New/Existing iLEC services can be design to new Metro 3.0 – fully interoperable to iLEC
  Support wireless backhaul , Wholesale Ethernet, MOE services

## Slide 4: BGP-LU for colorless
  BGP-LU provides reachability between iLEC and Metro 3.0 by advertising PE loopbacks
  BGP-LU in turn advertises the loopbacks and label bindings to remote MEs/MERs/MGR between the iLEC and metro Nodes
  BGP-Address Family (SAFI) L2VPN – advertises VPLS Route targets
  BGP-LU NNIs would replace FIN-E NNIs in Metro Markets – existing Services would be migrated
Metro 3.0
MGR
MC
MC
ILEC
MER-2
MGR-3
MER-1
BGP-RR
BGP-RR
BGP-LU
BGP-L2VPN
BGP-LU
Device | loopback | BGP-Label Unicast
ME3-1 | 1.1.1.1 | 1999345
ME3-2 | 1.1.1.2 | 1999347
ME3-3 | 1.1.1.3 | 1999386
Device | Loopback | BGP-Label Unicast
MER-1 | 10.2.2.1 | 2001342
MER-2 | 10.2.2.2 | 2002343
MGR-1 | 10.2.2.3 | 2003344
BGP-LU
BGP-LU
BGP-L2VPN
BGP-L2VPN
Nx100G
Nx100G

## Slide 5: Cell Site backhaul and colorless – priority #1
MCR
MCR
T-Mobile MSC
MER or MGR
8700
NID
100G upgrades already complete/near complete from previous T-Mobile requirement
MER
Metro 3.0/ECN
T-Mobile MSC
MER or MGR
8700
NID
MCR
MGR
MGR
MER
ILEC
vs
Metro 3.0
(colorless)
ILEC Waves
  Target is to support this design in 1H2021
  Upgrade iLEC MTSO handoff to 100G
  Build option-C 100G NNI between metro 3.0 and iLEC
  Build 100G Metro 3.0 network to Wire center on Inter office Fiber
  Deploy ECN to the Wire center
  Overbuild 10G NID to tower on iLEC F1/F2 Fiber
  Build VPLS service from MTSO(s) to ECN/NID
  Migrate from 1G to 10G
  Complete T-mobile upgrade by End of 2023

## Slide 6: Metro Direct + Metro Pop diversity - Priority#2
  Metro Direct – LAG and Transport Diversity – simple and scalable
  Pop Diversity – Support Service Redundancy / PE redundancy
  Metro Ring Diversity – Metro 3.0 will allow Ring to span between Pop/GWs
Metro 3.0
MGR
ILEC
MER-2
MGR-3
MER-1
MGW
Nx100G
Nx100G
BGP-RR
BGP-RR
BGP-LU
BGP-LU
BGP-L2VPN
Internet (3356)
MPLS (3549)
MPLS (209)
Metro Direct Transport + LAG redundancy
Pop#1
Pop#2

## Slide 7: Colorless Metro – Roadmap
HLD for Colorless Metro – published last Month
T-Mobile 10G Tower upgrade Business Case – based on Colorless
IT developing an OSS and BSS LOE and present to Leadership team
10G NID RFP in progress lower the cost of NID from ~ $1500 to $500 – Target for completion 2H21
Indoor and Outdoor Variants
10G and 100G Variants
Dual Vendor NID strategy
Programmability Direct to device API
Metro hardware RFP - Target for completion 2H21
100G and 400G Metro Core and Distribution
Spine Leaf/Ring design for scale
Segment Routing with VPLS - EVPN in future
Lower the $/G < $10, iLEC is currently ~ $60
Programmability Direct to device API

## Slide 8: Cell Site MTSO on Colorless – priority #2
MCR
MCR
T-Mobile MSC
MER or MGR
8700
NID
MER
Metro 3.0/ECN
T-Mobile MSC
MER or MGR
8700
NID
MCR
MGR
MGR
MER
ILEC Waves
Metro 3.0/ECN
MCR
MCR
T-Mobile MSC
MER
MER
ILEC Waves
M3
NCS
-
5501
M3
NCS
-
5501
M3
NCS
-
5501
M3
NCS
-
5501
T-Mobile MSC
ILEC MTSO
iLEC Metro with 3 G EVC/10G UNI
ILEC MTSO
Metro 3.0 with 10G EVC/10G UNI
Metro 3.0 MTSO
iLEC Metro with 3 G EVC/10G UNI
Metro 3.0 MTSO
Metro 3.0 with 10G EVC/10G UNI

## Slide 9
Colorless Metro Development Roadmap
Approved Projects / Already Underway
Future Phases / Pending Approval
Target Launch
NetDev
systems
PI8
PI9
PI10
PI11
PI12
Q2 2020
Q3 2021
Q4 2021
Q1 2022
Q2 2022+
Second vendor 100G ECN/M3 (RFP)
Low cost 10G NID (RFP)
BGP/VPLS for ECN
Cell site backhaul Y.1564 T&T
LOE – IT DEV
BGP-LU support for iLEC-Metro3.0
400G/100G MCR/MDR ( RFP)
10G Port based Dual EVCs on 10G NID
Cell site backhaul Y.1731
Colorless HLD
Metro Hardware
Metro Features
M3 for MTSO Head end
M3 Large – Dense 100G (RFP)
Service Config for NID/ECN
Dev TIRKS / ARM /OminVue
Sync Engine
Service Config M3 MTSO
Service Config Low cost 10G NID (RFP)
Service Config 100G ECN/M3 (RFP)